## Slide 1
MINOR PROJECT PRESENTATION
ON
TRAFFIC LIGHT CONTROL SYSTEM
USING
MICROCONTROLLER PIC 16F877A
MENTORS: SUBMITTED BY:
Mr. PAWAN LOCHAB AKANKSHA GUPTA , ECE-2 (14413202810)
Mr. PARVEEN KUMAR ISHITA GUPTA, ECE-2 (14813202810)
R.ASHOK KUMAR, ECE-2 (25013202810)
ARUN KUMAR, ECE-2 (01313207311)

## Slide 2: OBJECTIVE
TO DESIGN AND DEVELOP A SMART TRAFFIC LIGHT CONTROLLER USING MICROCONTROLLER PIC 16F877A

## Slide 3
The project uses:-
LED as TRAFFIC LIGHT indicator
MICROCONTROLLER for auto change of signal
Microcontroller PIC 16F877A is the brain of the project.
The LED’s are automatically on and off by making the corresponding port pin of the micro controller high.
Seven segment display- shows timing of each signal
During transition from green to red, the yellow led glows.
This process continues as a cycle.
BRIEF DESCIPTION

## Slide 4
AFTER 35 SEC
AFTER
15 SEC
AFTER
5 SEC
CYCLIC ROTATION

## Slide 5
MICRO
CONTROLLER
(PIC 16F877A)
7 SEGMENT DISPLAY
TRAFFIC LIGHTS
POWER SUPPLY
+5 VOLTS
BLOCK DIAGRAM

## Slide 6
CONNECTION DIAGRAM
Lane 1
BCD to decimal decoder
Lane 3
Lane 2
Lane 4
Seven Segment Display

## Slide 7: FLOW CHART

## Slide 8
AVAILABLE MICROCONTROLLERS
8051
AVR ATMEGA SERIES
PIC MICROCONTROLLERS
MICROCONTROLLER USED
PIC 16F877A
Characteristics
  Operating speed: 20 MHz
  Operating voltage: 4.0-5.5V
  Flash Memory: 14.3 Kbytes
  Data SRAM: 368 bytes
  Data EEPROM: 256 bytes
HARDWARE TOOLS
MICROCONTROLLER

## Slide 9
Special Microcontroller Features
  Self-reprogrammable under software control
  Watchdog Timer with on-chip RC oscillator
  Power-saving Sleep mode
  Selectable oscillator options
Advantages of PIC 16F877A over other microcontrollers
  RISC architecture
  In built ADC
  Noise immune
  Compiler for PIC has inbuilt function facility
  Low cost software solution

## Slide 10
PIN DIAGRAM OF PIC 16F877A

## Slide 11
AVAILABLE USB ASP PROGRAMMERS
PICKIT 1
PICKIT 2
PICKIT 3
PROGRAMMER USED
PICKIT 2
Features of PICKIT 2
• Separate programmer/debugger unit
• Open to the public
• Programmer-To-Go
• 128K byte memory
USB PROGRAMMER

## Slide 12
OTHER HARDWARES
VOLTAGE REGULATOR (IC 7805)
RESISTOR
CAPACITOR
BERG CONNECTOR
LED
SEVEN SEGMENT DISPLAY
  Voltage regulator Berg connector

## Slide 13
AVAILABLE IDE SOFTWARES
MPLAB
mikroC PRO
IDE USED
mikroC PRO
Features of mikroC PRO
mikroC PRO is easy to use as compared to MPLAB
Covers all PIC 12F, 16F , 18F family
Easy to maintain and modify
Includes documents, datasheets, images and drawings inside the code
SOFTWARE TOOLS
IDE SOFTWARE

## Slide 15
AVAILABLE EDA SOFWARES
PROTEUS
ORCAD
EAGLE
EDA USED
PROTEUS
Components of PROTEUS
• ISIS Schematic Capture - a tool for entering designs.
• PROSPICE - Mixed mode SPICE simulation
• ARES PCB Layout - PCB design system with:
1. Automatic component placer
2. Rip-up and retry auto-router
EDA SOFTWARE

## Slide 17: program
void main() { int i,a; TRISA=0X01; TRISB=0x00; TRISC=0x00; TRISD=0x00; while(1) { a=0x50; PORTB=0x1C; PORTC=0x11; for(i=0;i<=14;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } PORTB=0x14; PORTC=0x11; for(i=14;i<=49;i++) { PORTD=a; a=a--; delay_ms(100); | if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } PORTD=0x00; PORTB=0x12; a=0x05; for(i=0;i<=4;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } a=0x50; PORTB=0xC1; PORTC=0x11; for(i=0;i<=14;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { | a=a-6; } } PORTB=0x41; PORTC=0x11; for(i=14;i<=49;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } PORTD=0x00; PORTB=0x21; a=0x05; for(i=0;i<=4;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } }

## Slide 18
a=0x50; PORTB=0x11; PORTC=0x1C; for(i=0;i<=14;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } PORTB=0x11; PORTC=0x14; for(i=14;i<=49;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } PORTD=0x00; | PORTC=0x12; a=0x05; for(i=0;i<=4;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } a=0x50; PORTB=0x11; PORTC=0xC1; for(i=0;i<=14;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } PORTC=0x41; PORTB=0x11; | for(i=14;i<=49;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } PORTD=0x00; PORTC=0x21; a=0x05; for(i=0;i<=4;i++) { PORTD=a; a=a--; delay_ms(100); if(a==0x2F¦¦a==0x1F¦¦a==0x0F¦¦a==0x3F¦¦a==0x4F) { a=a-6; } } } }

## Slide 19: FUTURE SCOPE
This project can be enhanced in such a way as to automatically control the signals depending on the traffic density on the roads using sensors like IR detector/receiver module extended with automatic turn off when no vehicles are running on any side of the road which helps in power consumption saving.